## Slide 1: Code and Control Flow Integrity on Embedded systems
Academic Supervisor: Dr. Osnat Keren
Instructor: Gilad Dar
Project Team: Avihay Grigiac, Itai Riven

## Slide 2: Outline
Background
Objective
Literature Review
Setup Work Environment
Implement Existing Solution
Test Results
Improvements suggestion

## Slide 3: Background
The technology has reached almost every
aspects of our life
Health - Bionic body parts
Transportation – Autonomous cars
Security – cameras & security systems
IoT’s
The dependency on those technologies
binds us to find a reliable protection

## Slide 4: Background
Embedded systems
microcontroller-based system with a dedicated function
Problem Formulation
Most of the system’s modules are reliable and secure
Insider attacker can inject faults and cause an error – an arbitrary number of bits flip denoted by (a faulty instruction is )
RAM
Processor
Compiler
Device
programmer
ROM
Memory

## Slide 5: Outline
Background
Objective
Literature Review
Setup Work Environment
Implement Existing Solution
Test Results
Improvements suggestion

## Slide 6: Objective
Design an add-on hardware module for embedded systems for detecting malicious errors in a program
Requirements
Minimal affect on device performance
Minimal existing architectural changes
Minimal hardware costs
Minimal error masking probability
RAM
Processor
Compiler
Device
programmer
ROM
Memory
Protection

## Slide 7: Outline
Background
Objective
Literature Review
Setup Work Environment
Implement Existing Solution
Test Results
Improvements suggestion

## Slide 8: Definitions
Basic block an arbitrary number of sequential instructions which can only be entered at the ﬁrst and exited after the last instruction.
Control Flow Integrity (CFI) is a term for computer security techniques which prevent attacks by monitoring the program ﬂow.
Software Integrity (SI) is a security policy that prevents the execution of tampered software on the processor.
Notes: בסיק בלוק מאפשר לנו לעבוד ברזולוציה גבוהה יותר, במקום להתייחס לכל פקודה בנפרד הבסיק בלוק מאפשר לנו להתייחס לכל קבוצה של פקודות וכך להקטין את העלות של החומרה
CFI: נועד לגלות התקפה שמתחרשת על הזרימה של התוכנית על ידי מעקב אחר ריצת התוכנית
SI: נועד לגלות התקפה שמתרחשת על הפקודות שבתוך הבסיק בלוק ומונע את הביצוע של הפקודה

## Slide 9: Existing Solutions
Control Flow Graph - model normal program’s flow, each node in the graph represents a basic block and each edge is a valid transition
Continuous Signature Monitoring - set a signature for each instruction and verifying it at runtime before the execution of the instruction
Ensuring Code and Control-Flow Integrity means that all instructions in a basic block are executed correctly and the flow between basic blocks is valid
Notes: אחת הדרכים לבצע בקרה של ה-Control flow היא CFG, על ידי מיפוי של מעברים חוקיים נוכל לעקוב אחר המעברים בזמן אמת ולבדוק אם הם תואמים לגרף
והדרך להבטיח את התקינות של ביצוע הפקודות שבתוך הבסיק בלוק היא CSM
בפרוייקט שלנו אנחנו רוצים להבטיח את 2 הדברים, מעבר תקין בין כל בסיק בלוק וגם שכל פקודה בבלוק מתבצעת בצורה תקינה

## Slide 10: Code & control flow integrity
Software based CFI
Pros
  Cheap cost
  Easy implementation
Cons
  High overhead
  Vulnerable protection
Hardware based CFI
Pros
  Parallelism
  Isolated protection
Cons
  Expensive hardware cost
Notes: Software:
המימוש מתבצע על גבי רכיבים שכבר קיימים במערכתו והוא פשוט למימוש
עבור כל בדיקה המערכת "תעצור את פעולתה", עלות ביצועים גבוהה, התוקף יכול לתקוף את קוד ההגנה עצמו שנמצא באותו הזיכרון.

## Slide 11: Code & control flow integrity – how it works
“Protecting the Control Flow of Embedded Processors against Fault Attacks” By Mario Werner, Erich Wenger & Stefan Mangard
Part 1: Compilation
  Calculate the signature of each basic block
  Determine valid flow between basic blocks
Part 2: Runtime
  Hardware module calculates the signature for each instruction
  Check the validity at pre-defined points
Device
RAM
Processor
Compiler
ROM
Memory
Derived Signature
Protected Memory

## Slide 12: Code & control flow integrity – how it works (cont’)
Signature function - Cyclic Redundancy Checks(CRCs)
Calculate the signature value
Update Function – XOR
Keep the signature value the same, independent
of the used paths

## Slide 13: Future Work
Background
Objective
Literature Review
Setup Work Environment
Implement Existing Solution
Test Results
Improvements suggestion
March
March - April
May
June - July